## Slide 1: Pinpointing Performance Inefficiencies via Lightweight Variance Profiling
Pengfei Su
College of William and Mary
Milind Chabbi
Scalable Machines Research
Xu Liu
College of William and Mary
Shuyin Jiao
College of William and Mary

## Slide 2: Complexity in HPC Software
Complexities
Large amount of source code
Hierarchies of component libs
Sophisticated control/data flow
Unpredictable hardware performance (cache, network)

## Slide 3: The Landscape of Application Performance and Performance Tools
Fast
Always
Slow
Sometimes
✘: Slow instances of a function are hidden due to averages
Variance detection can bubble up functions behaving erratically
Use any performance tool
You are a genius, don’t waste your time in this session
Listen to
the rest of
the talk

## Slide 4: Why Detect Variance
Detect performance anomalies
  Especially in latency sensitive applications, e.g., “long tail” latency
Necessary for performance predictability
  Especially in high performance applications using asynchrony
Avoid getting washed by averages
Proven technique in enterprise workloads
  VProfiler [Huang et al. Eurosys’17]

## Slide 5: Previous Focus vs. Our Focus
Previous focus
  Variance of resource usage in MPI functions across different nodes
  Rely on function-level instrumentation
Our focus
  Variance of resource usage within a node across different invocations of the same function
  Rely on sampling hardware performance monitoring units (PMU)

## Slide 6: Motivating Example — GTC
Particle-in-cell code for simulations
Previous study[1]: traverse() introduce cache misses as program executes
[1] G Marin, G Jin, and J Mellor-Crummey. 2008. Managing locality in grand challenge applications: a case study of the gyrokinetic toroidal code. Journal of Physics: Conference Series 125 (jul 2008), 012087.
ith invocation of traverse()
Cache misses

## Slide 7: Motivating Example — GTC
Variance analysis
  traverse() accesses particles sequentially: particle1->particle2->…
Optimization
  Sort particles periodically
  ~20% speedup
particle1 | particle2 | particle3 | particle4 | particle5 | particle6
particle1 | particle4 | particle2 | particle6 | particle5 | particle3
Access order = storage order
…
Access order storage order
Loss of data locality
Good data locality
Storage:
Storage:
Timeline
Access:
Access:

## Slide 8: Function Variance Detection
Prerequisite
  Place calipers at function entry and exit to identify function boundary
    Measure the resource usage in a function
main()
Function entry
funA()
Function exit
Measure resource usage: r1
Measure resource usage: r2
Resources consumed in funA() = r2 - r1
Timeline
main() {
funA();
}

## Slide 9: Function Variance Detection
Previous effort
  Instrumentation-based tools
    Instrument function entry and exit to identify function boundary
main()
Function entry
funA()
Function exit
1st instrumentation point
2nd instrumentation point
Timeline
main() {
funA();
}
✔️: high accuracy
✘: high overhead (~2x)
Resources consumed in funA()

## Slide 10: Difficulty in Detecting Variance via Sampling
  Sampling-based tools cannot synchronize sampling with function call and return from the same function instance
main()
funA()
✔️: low overhead
✘: low accuracy
Timeline
sampling point
sampling point
Function entry
Function exit
funA()
sampling point
sampling point

## Slide 11: What Sampling Tools Need for Variance Detection
The ability to randomly sample function calls
  But no instrumentation on function entry or exit
The ability to synchronize “start monitoring” with function call
The ability to synchronize “stop monitoring” with function return

## Slide 12: FVSampler
A sampling-based function execution variance detection tool
  Lightweight
    6% (time)
    7 MB/thread (memory)
  Accurate
    Synchronize sampling with function boundary to monitor whole function instances
  Insightful
    Provide full calling context to drilldown the call paths of high variance
    Measure variance in various performance metrics, e.g., CPU cycles, cache misses, retired instructions

## Slide 13: What Sampling Tools Need for Variance Profiling
The ability to randomly sample function calls
  But no instrumentation on function entry or exit
The ability to synchronize “start monitoring” with function call
The ability to synchronize “stop monitoring” with function return
︖
︖

## Slide 14: Performance Monitoring Units (PMUs)
Available in commodity CPU
Monitor hardware events
Can be configured to monitor function call events
Provide two modes
  Counting mode: count # of occurrences of an event
  Sampling mode: deliver a sample (interrupt) every N occurrences of an event

## Slide 15: What Sampling Tools Need for Variance Profiling
The ability to randomly sample function calls
  But no instrumentation on function entry or exit
The ability to synchronize “start monitoring” with function call
The ability to synchronize “stop monitoring” with function return
✔️
✔️
︖

## Slide 16: Debug Register
Available in commodity CPU
Trap program execution when a designated address (watchpoint) is touched
  Intercept function return

## Slide 17: What Sampling Tools Need for Variance Profiling
The ability to randomly sample function calls
  But no instrumentation on function entry or exit
The ability to synchronize “start monitoring” with function call
The ability to synchronize “stop monitoring” with function return
✔️
✔️
✔️

## Slide 18: Methodology
Observation
main() {
funA();
}
main()
funA()
Call
…
main()
Stack register
RSP
Stack frame
Parameters
Ret address
funA()
Stack register
RSP
Stack register
RSP
main()
funA()
Return
Ret instruction
Read
Stack growth

## Slide 19: Methodology
Synchronize sampling with function boundaries
  Configure PMU to sample function call
  Use a debug register to set a watchpoint at addr[RSP] to intercept function return
…
RSP
main()
funA()
Function call
Parameters
Ret address
Ret address
…
main()
funA()
Function return
Parameters
Ret address
Ret address
Ret instruction
Read
Watchpoint trap
Watchpoint
Stack growth
Stack growth

## Slide 20: Methodology
Count resource usage of a function invocation instance
  Read PMU to count resources (r1) used by the program at function call
  Read PMU to count resources (r2) used by the program at function return
Resource usage in funA() = r2 - r1
…
RSP
main()
funA()
Function call
Parameters
Ret address
Ret address
…
main()
funA()
Function return
Parameters
Ret address
Ret address
Ret instruction
Read
Watchpoint trap
Watchpoint
main() {
funA();
}
Stack growth
Stack growth

## Slide 21: Challenge
x86 CPU offers 4 debug registers
  Limitation: monitor at most 4 functions simultaneously
Watchpointmain
main()
funA()
funB()
funC()
funD()
WatchpointfunA
WatchpointfunB
WatchpointfunC
No debugs!
Call chain: main()->funA()->funB()->funC()->funD()

## Slide 22: Challenge
x86 CPU offers 4 debug registers
  Solution: maintain a shadow stack to save active watchpoints
    Require only 1 debug register
main() {
funA();
}
…
Shadow stack
Watchpointmain
main()

## Slide 23: Challenge
x86 CPU offers 4 debug registers
  Solution: maintain a shadow stack to save active watchpoints
    Require only 1 debug register
main() {
funA();
}
…
Shadow stack
Watchpointmain
main()
funA()
WatchpointfunA
main()
funA()
Return

## Slide 24: Other Challenges in the Paper
Concurrently monitor multiple functions and recursions
setjmp()/longjmp()
Online variance calculation
Highlight variance of statistically significant functions
Calling context collection
Parallelism (multithreading/multiprocessing)

## Slide 25: Experiments
Time overhead
1.06x
Notes: Lower is better/
Quite common.
These two figures show the distribution of temporal and spatial load redundancy on SPEC 2006.
We can see that redundant loads, especially the temporal ones are quite common. Typically, each one offers some unique opportunity to optimize. Eliminating a few top ones often yield non-trivial speedups. However, redundancy doesn’t mean it is redundant on every execution path, users need to figure out a safe optimization.

## Slide 26: Experiments
Per-sample overhead
50 µs
Notes: Lower is better/
Quite common.
These two figures show the distribution of temporal and spatial load redundancy on SPEC 2006.
We can see that redundant loads, especially the temporal ones are quite common. Typically, each one offers some unique opportunity to optimize. Eliminating a few top ones often yield non-trivial speedups. However, redundancy doesn’t mean it is redundant on every execution path, users need to figure out a safe optimization.

## Slide 27: Case Study
Program | Inefficiencies | Optimization | Speedup
Sequoia AMG2006 | Load imbalance | Reducing the granularity of parallel work | 1.08×
MASNUM | Linear search | Locality-friendly search | 1.54×
NERSC-8 MiniFE | Poor data structure | Replacing C++ set with unordered_set | 1.96×
Parsec-2.1 dedup | Poor hashing algorithm | Reducing hash collisions | 1.08x
Program | Inefficiencies | Optimization | Speedup
Sequoia AMG2006 | Load imbalance | Reducing the granularity of parallel work | 1.08×
MASNUM | Linear search | Locality-friendly search | 1.54×
NERSC-8 MiniFE | Poor data structure | Replacing C++ set with unordered_set | 1.96×
Parsec-2.1 dedup | Poor hashing algorithm | Reducing hash collisions | 1.08x

## Slide 28: Case Study — MASNUM
Forecast ocean surface waves
ACM Gordon Bell Prize finalists
Calling context
Source code
Variance metric
Variance of instruction #
Function
Notes: Lower is better/
Quite common.
These two figures show the distribution of temporal and spatial load redundancy on SPEC 2006.
We can see that redundant loads, especially the temporal ones are quite common. Typically, each one offers some unique opportunity to optimize. Eliminating a few top ones often yield non-trivial speedups. However, redundancy doesn’t mean it is redundant on every execution path, users need to figure out a safe optimization.

## Slide 29: Case Study — MASNUM
Variance of instructions # in different invocations of search()
ith invocation of search()
# of instructions
Two takeaways:
1) # of instrs has a periodical distribution pattern
2) In each period, # of instrs (i.e., workload) in adjacent invocations are similar
Notes: Lower is better/
Quite common.
These two figures show the distribution of temporal and spatial load redundancy on SPEC 2006.
We can see that redundant loads, especially the temporal ones are quite common. Typically, each one offers some unique opportunity to optimize. Eliminating a few top ones often yield non-trivial speedups. However, redundancy doesn’t mean it is redundant on every execution path, users need to figure out a safe optimization.

## Slide 30: Case Study — MASNUM
Investigation of search()
  search() performs a linear search for each input over an array
  Inputs in adjacent invocations are similar
target array = {1, 2, 3, 4, 5}
input = {2, 2, 3, 3}
✔️
input = {2, 2, 3, 3}:
1 | 2 | 3 | 4 | 5
1 | 2 | 3 | 4 | 5
1 | 2 | 3 | 4 | 5
search()
✔️
input = {2, 2, 3, 3}:
1 | 2 | 3 | 4 | 5
1 | 2 | 3 | 4 | 5
1 | 2 | 3 | 4 | 5
search()
✔️
input = {2, 2, 3, 3}:
1 | 2 | 3 | 4 | 5
1 | 2 | 3 | 4 | 5
1 | 2 | 3 | 4 | 5
search()
1 | 2 | 3 | 4 | 5
✔️
input = {2, 2, 3, 3}:
1 | 2 | 3 | 4 | 5
1 | 2 | 3 | 4 | 5
1 | 2 | 3 | 4 | 5
search()
1 | 2 | 3 | 4 | 5
# of comparisons in adjacent invocations are similar
# of instructions in adjacent invocations are similar
Notes: Lower is better/
Quite common.
These two figures show the distribution of temporal and spatial load redundancy on SPEC 2006.
We can see that redundant loads, especially the temporal ones are quite common. Typically, each one offers some unique opportunity to optimize. Eliminating a few top ones often yield non-trivial speedups. However, redundancy doesn’t mean it is redundant on every execution path, users need to figure out a safe optimization.

## Slide 31: Case Study — MASNUM
Optimization
  Locality-friendly search
    Start from the location where the previous search finishes
    Speedup: 54%
    Variance: 35% -> 2%
ith invocation of search()
(1) Variance before optimization
ith invocation of search()
(2) Variance after optimization
# of instructions
# of instructions
Notes: Lower is better/
Quite common.
These two figures show the distribution of temporal and spatial load redundancy on SPEC 2006.
We can see that redundant loads, especially the temporal ones are quite common. Typically, each one offers some unique opportunity to optimize. Eliminating a few top ones often yield non-trivial speedups. However, redundancy doesn’t mean it is redundant on every execution path, users need to figure out a safe optimization.

## Slide 32: Case Study — Parsec Decup
(1) Variance before optimization
(2) Variance after optimization
ith invocation of hashtable_search()
ith invocation of hashtable_search()
Notes: Lower is better/
Quite common.
These two figures show the distribution of temporal and spatial load redundancy on SPEC 2006.
We can see that redundant loads, especially the temporal ones are quite common. Typically, each one offers some unique opportunity to optimize. Eliminating a few top ones often yield non-trivial speedups. However, redundancy doesn’t mean it is redundant on every execution path, users need to figure out a safe optimization.

## Slide 33: Conclusions
FVSampler
  Pinpoints function execution variance with low overhead
  Advances the state-of-the-art by demonstrating the ability to synchronize sampling with function boundary
  Addresses challenges arising due to combining the usage of PMUs and debug registers
  Provides rich insights to identify and optimize unpredictable code performance
  Available at https://github.com/WitchTools/FVSampler
Questions?